## Slide 1
Memory Address
Programming model
General purpose register (GPR) 當CPU程序運作中， 實際參與計算、輔助運行時的內部暫存器。
Segment register 系統設定暫存器或使用者自定義暫存器。
Status and instruction register CPU指令設定及儲存之系統暫存器。
GPR 1.)
Status and instruction register 2.)
Segment register 3.)
※Reference: 1. “TMS320C28x CPU and Instruction Set”; 2.“TMS320F2837xD Delfino Microcontrollers”; 3. “TMS320F2837xD Dual-Core Microcontrollers datasheet (Rev. O)”.

## Slide 2
Data-addressing Modes
Register
Immediate
Direct
Register indirect
Base-plus-index
Register relative
Base relative-plus-index
Scaled index

## Slide 3
Mode | Instruction | Code
Register | MOV AX,BX | MOV AH,AL
Immediate | MOV CH,3AH | MOV AH,#100
MOV AR0,#0000000001100100b
MOV T,#0x0064
Direct | MOV [1234H],AX | MOVW DP,#Timerpage MOV @TIMER0PRD,AH
MOV *(0x0C02),AH
Register indirect | MOV [BX],CL | MOV AR0,#TIMER0PRD MOV *AR0,AH
Register relative | MOV CL,[BX+4] | MOVW DP,#Timerpage MOV @TIMER0PRD+1,AH
Data-addressing Modes
※ Reference : “TMS320F2837xD Delfino Microcontrollers”, Chapter 6.7.2, Table 6-7

## Slide 4
Common Code instructions： Operator(ADD, SUB, ABS…), MOV, Branch ※TMS320C28x CPU and Instruction Set, Chapter 6, C28x Assembly Language Instructions .
Data segment setting：
Built up memory page.
Set self-definition register, name & memory address.
Assembly Language Instructions
※ Reference : “TMS320C28x CPU and Instruction Set”.

## Slide 5
組合語言語法與定址模式說明
所有功能說明與暫存器使用說明
Datasheet introduce

## Slide 6
通用輸入輸出腳位說明
Datasheet introduce

## Slide 7
實驗說明：
範例題：使用Timer1計時器，產生週期為10u sec之中斷，並以GPIO2
在每次進入中斷時將GPIO 2 拉高電位；在每次離開中斷時將
GPIO 2 拉低電位。
實驗題：利用Timer1計時器，產生週期為100u sec之中斷，以每4次Timer1
中斷進入1次Timer2中斷，並以GPIO 2及GPIO 3 I/O腳分別觀察
Timer1與Timer2之中斷時間，及觀察兩個Timer中斷之優先權 。
實習一
整體晶片運作必先設定時脈 => Clocking__3.7章節
CPU Timer 模組功能設置__3.8章節
通用輸入輸出腳位, F28379D Overview pdf
中斷功能設置__3.4章節

## Slide 8
3.7 Clocking

## Slide 9
3.7 Clocking

## Slide 10
3.8 CPU Timer

## Slide 11
3.8 CPU Timer

## Slide 12
What is Interrupt
Initial setup
Software execution flow
Main loop
Setup system clock, setup module, setup peripheral…
Reset register, I/O state…
Do nothing, waiting for interrupt
When an interrupt occurred
Interrupt code execution
Return to main loop
Interrupt

## Slide 13
What is Interrupt
Initial setup
Software execution flow
Main loop
Setup system clock, setup module, setup peripheral…
Reset register, I/O state…
Do nothing, waiting for interrupt
When multiple interrupt occurred
Interrupt with highest priority executes first
Return to main loop
Interrupt with lower priority executes
Interrupt 1
Interrupt 2
Interrupts switch timing depends on EINT setting

## Slide 14
EINT setting
Interrupts timing with / without EINT
Description | Execution timing
Interrupt 1: with “EINT” |  |  | 
Interrupt 2: |  |  | 
Scenario 1:
Interrupt2 “interrupts” interrupt1
Interrupt2 has finished
return to interrupt1
Description | Execution timing
Interrupt 1: No “EINT” |  | 
Interrupt 2: |  | 
Scenario 2:
Interrupt2 is waiting for interrupt1 to finish

## Slide 15
3.4 Peripheral Interrupt
Interrupt “Group”
Interrupt “Member”

## Slide 16
3.4 Peripheral Interrupt
IER: Enable
IFR: Flag
INTM: Master
PIEACK: Acknowledge
Interrupt Member
Interrupt Group

## Slide 17
3.4 Peripheral Interrupt
Direct link to CPU
“MUXed” see last page

## Slide 18
3.4 Peripheral Interrupt

## Slide 19
Interrupt Priority

## Slide 20
GPIO

## Slide 21
6 GPIO

## Slide 22
實習一
實驗說明
範例題：使用Timer1計時器，產生週期為10u sec之中斷，並在每次進入中斷時將GPIO 3 拉高電位；在每次離開中斷時將GPIO 3 拉低電位。
(系統頻率為200MHz)
實驗題：利用Timer1計時器，產生週期為100u sec之中斷，並在每次進入中斷
將GPIO 3 拉高電位；在每次離開中斷時將GPIO 3 拉低電位。
利用Timer2計時器，產生週期為400u sec之中斷，並在每次進入中斷
將GPIO 4 拉高電位；在每次離開中斷時將GPIO 4 拉低電位。
以示波器查看GPIO 3及GPIO 4 波形並觀察Timer1和Timer2之中斷時間，以及觀察兩個Timer中斷之優先權 。
(系統頻率為100MHz)
繳交期限:2024/10/7
作業繳交: google classroom
課程代碼: gs4fyai
問題請洽:
助教信箱:t113318009@ntut.org.tw

## Slide 23
實驗波形
不允許中斷插入
允許Timer1中斷插入Timer2中斷
本次作業請做出允許中斷插入(右邊波形)