## Slide 1: F2837xD Workshop
Technical Training Organization
Copyright © 2014 Texas Instruments. All rights reserved.
C2000 is a trademark of Texas Instruments.

## Slide 2: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 3: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 4: Required Workshop Materials
http://processors.wiki.ti.com/index.php/F2837xD_Workshop
F2837xD Experimenter’s Kit
Install Code Composer Studio v6.0.1
Run the workshop installer
  F2837xD Workshop-1.1-Setup.exe
    Lab Files / Solution Files
    Student Guide and Documentation

## Slide 5: F28377D controlCARD
SW1: Boot Modes
SW2: External VREFHI disable
TMS320F28377D
A:J1 - USB emulation/ UART
J8: Host/ Device
XDS100v2 emulation and isolation circuitry
A:SW1 - isolated emulation and UART communication enable switch
U5: µSD card
LED LD2: GPIO31 (red)
LED LD3: GPIO34 (red)
LED LD1: Power (green)
J2 - J7: USB PHY connection enable jumpers
SW3: ADC VREFHI ADC A & B
SW4: ADC VREFHI ADC C & D

## Slide 6: F28x7x Piccolo / Delfino Comparison
 | F2807x | F2837xS | F2837xD
C28x CPUs | 1 | 1 | 2
Clock | 120 MHz | 200 MHz | 200 MHz
Flash / RAM / OTP | 256Kw / 50Kw / 2Kw | 512Kw / 82Kw / 2Kw | 512Kw / 102Kw / 2Kw
On-chip Oscillators |  |  | 
Watchdog Timer |  |  | 
ADC | Three 12-bit | Four 12/16-bit | Four 12/16-bit
Buffered DAC | 3 | 3 | 3
Analog COMP w/DAC |  |  | 
FPU |  |  |  (each CPU)
6-Channel DMA |  |  |  (each CPU)
CLA |  |  |  (each CPU)
VCU / TMU |  /  |  /  |  /  (each CPU)
ePWM / HRPWM |  /  |  /  |  / 
eCAP / HRCAP |  /  |  /  |  / 
eQEP |  |  | 
SCI / SPI / I2C |  /  /  |  /  /  |  /  / 
CAN / McBSP / USB |  /  /  |  /  /  |  /  / 
UPP | - |  | 
EMIF | 1 | 2 | 2

## Slide 7: F28x Piccolo / Delfino Comparison
 | F2806x | F2833x | F2837xD
C28x CPUs | 1 | 1 | 2
Clock | 90 MHz | 150 MHz | 200 MHz
Flash / RAM / OTP | 128Kw / 50Kw / 1Kw | 256Kw / 34Kw / 1Kw | 512Kw / 102Kw / 2Kw
On-chip Oscillators |  | - | 
Watchdog Timer |  |  | 
ADC | One 12-bit (SOC) | One 12-bit (SEQ) | Four 12/16-bit (SOC)
Buffered DAC | - | - | 3
Analog COMP w/DAC |  | - | 
FPU |  |  |  (each CPU)
6-Channel DMA |  |  |  (each CPU)
CLA |  | - |  (each CPU)
VCU / TMU |  / - | - / - |  /  (each CPU)
ePWM / HRPWM |  /  |  /  |  / 
eCAP / HRCAP |  /  |  / - |  / 
eQEP |  |  | 
SCI / SPI / I2C |  /  /  |  /  /  |  /  / 
CAN / McBSP / USB |  /  /  |  /  / - |  /  / 
UPP | - | - | 
EMIF | - | 1 | 2

## Slide 8: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 9: F2837xD – Dual Core Block Diagram

## Slide 10: TMS320F28x7x Core Block Diagram
Sectored
Flash
Program Bus
Data Bus
RAM
Boot
ROM
3
32-bit
Timers
PIE Interrupt Manager
eQEP
Watchdog
I2C
SCI
SPI
GPIO
eCAP
CLA
CAN 2.0B
ADC
CLA Bus
32x32 bit
Multiplier
FPU
CPU
Register Bus
R-M-W
Atomic
ALU
TMU
VCU
DMA
6 Ch.
DMA Bus
McBSP
ePWM
USB 2.0
EMIF
Multichannel
Buffered Serial
Ports
External Memory
Interfaces
Trigonometric
Math Unit
Viterbi/Complex
Math Unit
Programmable
Control Law
Accelerator

## Slide 11: F28x CPU + FPU + VCU + TMU and CLA
MCU/DSP balancing code density & execution time
  16-bit instructions for improved code density
  32-bit instructions for improved execution time
32-bit fixed-point CPU + FPU
32x32 fixed-point MAC, doubles as dual 16x16 MAC
IEEE Single-precision floating point hardware and MAC
Floating-point simplifies software development and boosts performance
Viterbi, Complex Math, CRC Unit (VCU) adds support for Viterbi decode, complex math and CRC operations
Parallel processing Control Law Accelerator (CLA) adds IEEE Single-precision 32-bit floating point math operations
CLA algorithm execution is independent of the main CPU
Trigonometric operations supported by TMU
Fast interrupt service time
Single cycle read-modify-write instructions
Data Bus
3
32-bit
Timers
CPU
Register Bus
Program Bus
32x32 bit
Multiplier
FPU
R-M-W
Atomic
ALU
CLA
CLA Bus
TMU
VCU
PIE
Watchdog

## Slide 12: Simplified F28x7x Memory Map
M0 RAM (1Kw)
M1 RAM (1Kw)
PIE Vectors (512w)
CLA to CPU MSG RAM (128w)
CPU to CLA MSG RAM (128w)
EMIF-2 (4Kw)
LS0 – LS5 RAM (2Kw each)
D0 – D1 RAM (2Kw each)
0x000000
0x000400
0x000D00
0x001480
0x002000
0x008000
0x00B000
0x001500
GS0 – GS15 RAM (4Kw each)
CPU2 to CPU1 IPC MSG RAM (1Kw)
CPU1 to CPU2 IPC MSG RAM (1Kw)
FLASH (256Kw)
User OTP (1Kw)
EMIF-1 (2.9Mw)
Boot ROM (32Kw)
BROM Vectors (64w)
0x00C000
0x03F800
0x03FC00
0x078000
0x080000
0x100000
0x3F8000
0x3FFFC0
LS0 – LS5 RAM
accessible by
CPU & CLA
GS0 – GS15
and EMIF1
accessible by DMA
(only GS0 – GS7
RAM on F2807x)
Notes:
Only EMIF-1 on F2807x
IPC MSG RAMs only on F2837xD
512Kw FLASH on F2837xS

## Slide 13: F28x Fast Interrupt Response Manager
192 dedicated PIE vectors
No software decision making required
Direct access to RAM vectors
Auto flags update
Concurrent auto context save
28x CPU Interrupt logic
28x
CPU
INTM
192
Peripheral Interrupts 12x16 = 192
12 interrupts
INT1 to INT12
PIE
Register
Map
PIE module For 192 interrupts
T ST0
AH AL
PH PL
AR1 (L) AR0 (L)
DP ST1
DBSTAT IER
PC(msw) PC(lsw)
Auto Context Save
IFR
IER

## Slide 14: Direct Memory Access (DMA)
McBSP
DMA
6-channels
ADC
Result 0-15
Triggers
PIE
DINTCH1-6
PWM1
PWM2
PWM11
PWM12
Transfers data between peripherals and/or memory without intervention from the CPU
GS0 RAM
GS15 RAM
EMIF
ADCA/B/C/D (1-4, EVT)
MXEVTA/B MREVTA/B
XINT1-5 TINT0-2
ePWM1-12 (SOCA-B)
SD1FLT1-4 SD2FLT1-4
SPITX/RX (A-C)
USBA_EPx_RX/TX1-3
software
IPC RAM
SPI

## Slide 15: Control Law Accelerator (CLA)
C28x CPU
CLA
PWM
ADC
&
CMP
An independent 32-bit floating-point math accelerator
Executes algorithms independently and in parallel with the main CPU
Direct access to ePWM, HRPWM, eCAP, eQEP, ADC result, CMPSS, DAC, SDFM, SPI, McBSP, and uPP registers
Responds to peripheral interrupts independent of the CPU
Frees up the CPU for other tasks (communications and diagnostics)

## Slide 16: Viterbi / Complex Math Unit (VCU-II)
Extends C28x instruction set to support:
Viterbi operations
  Decode for communications
Complex math
  16-bit fixed-point complex FFT
    used in spread spectrum communications, and many signal processing algorithms
  Complex filters
    used to improve data reliability, transmission distance, and power efficiency
  Power Line Communications (PLC) and radar applications
Cyclic Redundancy Check (CRC)
  Communications and memory robustness checks
  Other: OFDM interleaving & de-interleaving, Galois Field arithmetic, AES acceleration
VCU execution registers
VCU-II
VSTATUS
VR0
VR1
VR2
VR3
VR4
VR5
VR6
VR7
VR8
VT0
VT1
VCRC
SMO to SM63
Data path logic for VCU-II Instruction
General instructions
CRC instructions
Arithmetic instructions
Galois Field instructions
Complex FFT instructions
VCU II Control Logic
動態演算法
資料傳遞之可靠度

## Slide 17: Trigonometric Math Unit (TMU)
Supported by natural C and C-intrinsics
Significant performance impact on algorithms such as:
• Park/ Inverse Park • DQ0 Transform & Inverse DQ0
• Space Vector GEN • FFT Magnitude & Phase Calculations
Adds instructions to FPU for calculating common Trigonometric operations
x
y
r
y = r * sin(rad)
x = r * cos(rad)
r = sqrt(x2 + y2)
rad = atan(y/x)
Operation | Instruction | Exe Cycles | Result Latency | FPU Cycles w/o TMU
Z = Y/X | DIVF32 Rz,Ry,Rx | 1 | 5 | ~24
Y = sqrt(X) | SQRTF32 Ry,Rx | 1 | 5 | ~26
Y = sin(X/2pi) | PUSINF32 Ry,Rx | 1 | 4 | ~33
Y = cos(X/2pi) | PUCOSF32 Ry,Rx | 1 | 4 | ~33
Y = atan(X)/2pi | PUATANF32 Ry,Rx | 1 | 4 | ~53
Instruction To Support ATAN2 Calculation | QUADF32 Rw,Rz,Ry,Rx ATANPUF32 Ra,Rz ADDF32 Rb,Ra,Rw | 3 | 11 | ~90
Y = X * 2pi | MPY2PIF32 Ry,Rx | 1 | 2 | ~4
Y = X * 1/2pi | DIV2PIF32 Ry,Rx | 1 | 2 | ~4

## Slide 18: External Memory Interface (EMIF)
Provides a means for the CPU, DMA, and CLA to connect to various memory devices
Support for synchronous (SDRAM) and asynchronous (SRAM, NOR Flash) memories
F2837xD includes two EMIFs
  EMIF1 – 16/32-bit interface shared between CPU1 and CPU2
  EMIF2 – 16-bit interface dedicated to CPU1
Arbiter/
Memory
Protection
EMIF1
16/32-Bit
Interface
CPU1
CPU1.DMA1
CPU2
CPU2.DMA1
Arbiter/
Memory
Protection
EMIF2
16-Bit
Interface
CPU1
CPU1.CLA1
EMIF1 shared between CPU1 & CPU2
EMIF2 dedicated to CPU1

## Slide 19: Communication Peripherals
Four Serial Communication Interfaces (SCI) with 16-level deep TX/RX FIFOs
Three Serial Peripheral Interfaces (SPI) with 16-level deep TX/RX FIFOs
Two Inter-Integrated Circuit Interfaces (I2C) with 16-level deep TX/RX FIFOs
Two Multi-channel Buffered Serial Ports (McBSP) with double-buffered TX and triple-buffered RX
Two Controller Area Network Ports (CAN) with 32 mailboxes each
One USB + PHY port

## Slide 20: On-Chip Safety Features
Memory Protection
  ECC and parity enabled RAMs, shared RAMs protection
  ECC enabled flash memory
Clock Checks
  Missing clock detection logic
  PLLSLIP detection
  NMIWDs
  Windowed watchdog
Write Register Protection
  LOCK protection on system configuration registers
  EALLOW protection
  CPU1 and CPU2 PIE vector address validity check
Annunciation
  Single error pin for external signalling of error
error correction code

## Slide 21: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 22: Programming Model: Header Files & API
API Drivers
  C functions automatically set register bit fields
  Common tasks and peripheral modes supported
  Reduces learning curve and simplifies programming
Bit Fields
  C structures – Peripheral Register Header Files
  Register access whole or by bits and bit fields are manipulated without masking
  Ease-of-use with CCS IDE
Registers and Addresses
  Assembly language used to program hardware registers and access addresses
Hardware
Software
Registers and Addresses
Bit Fields
API Drivers
Direct use of header files
Hardware Abstraction
CPU and Peripherals  Header Files
USB & CAN  API Drivers

## Slide 23: Programming Model: Comparison
Device support package includes documentation and examples showing how to use the Bit Field Header Files or API Driver Library
Device support packages located at: C:\TI\controlSUITE\device_support\
controlSUITE located at http://www.ti.com and enter “controlSUITE” in the keyword search box
interrupt void IsrAdc(void)
{
//Period of ePWM1 is set in //init; Multiply period by //desired duty to get CMPA //value;
EPwm1Regs.CMPA.half.CMPA = EPwm1Regs.TBPRD * duty;
}
//Interrupts set up elsewhere
//Set duty cycle
MOVB @9,#0x0F,UNC
//Set PWM1A on Zero Event
AND AL,@11,#0xFFFC
ORB AL,#0x02
MOV @11,AL
//Clear PWM1A on Up-count //CompareA event
AND AL,@11,#0xFFCF
ORB AL,#0x10
MOV @11,AL
interrupt void IsrAdc(void)
{
/* set a new pwm value */
PWM_setDutyA(PWM_MODULE_2, duty);
}
Direct Register Access
Bit Field Header Files
API Driver

## Slide 24: Code Composer Studio: IDE
Integrates: edit, code generation, and debug
Single-click access using buttons
Powerful graphing/profiling tools
Automated tasks using Scripts
Based on the Eclipse open source software framework

## Slide 25: CCS – Software Development
Code Composer Studio includes:
  Integrated Edit/Debug GUI
  Code Generation Tools
  TI-RTOS
Asm
Link
Editor
Debug
Compile
Graphs,
Profiling
Code
Simulator
Development
Tool
External
Emulator
MCU
Board
Libraries
lnk.cmd
Build

## Slide 26: Edit and Debug Perspective
Each perspective provides a set of functionality aimed at accomplishing a specific task
Edit Perspective
  Displays views used during code development
    C/C++ project, editor, etc.
Debug Perspective
  Displays views used for debugging
    Menus and toolbars associated with debugging, watch and memory windows, graphs, etc.

## Slide 27: Creating a Target Configuration
File  New  Target Configuration File
Select connection type
Select device
Save configuration

## Slide 28: CCSv6 Project
List of files:
  Source (C, assembly)
  Libraries
  SYS/BIOS configuration file
  Linker command files
Project settings:
  Build options (compiler, assembler, linker, and TI-RTOS)
  Build configurations
Project files contain:

## Slide 29: Creating a New CCSv6 Project(s)
CPU1
CPU2
Advanced Setting / Project Templates and Examples
File  New  CCS Project

## Slide 30: CCSv6 Build Options – Compiler / Linker
Separate build options for each project – CPU1 & CPU2
Compiler
  Categories for code generation tools – controls many aspects of the build process, such as:
    Optimization level
    Target device
    Compiler / assembly / link options
Linker
  Categories for linking – specify various link options
  ${PROJECT_ROOT} specifies the current project directory

## Slide 31: Launching Dual Subsystem Debug (1)
1st subsystem (CCS Edit Perspective) -
  Clicking “Debug” button will automatically:
    Launch the debugger
    Connects to target
    Programs flash memory
Note 2nd subsystem is disconnected
Next step will connect 2nd subsystem

## Slide 32: Launching Dual Subsystem Debug (2)
2nd subsystem (CCS Debug Perspective) -
  In Debug window right-click on emulator and select “Connect target”
  Highlight emulator and load program (flash)
    Run  Load  Load Program…
Both subsystems are connected
Next step is dual subsystem start-up sequence

## Slide 33: Dual Subsystem Debug Start-up
Start-up sequence
  Reset CPU1 subsystem
  Reset CPU2 subsystem
  Run CPU1 subsystem
  Run CPU2 subsystem
  Stop and debug either subsystem
Debug window controls “selected” subsystem for the debug interaction
  Highlight appropriate subsystem for debug

## Slide 34: Lab File Directory Structure
All modified files are in the Project Folder
Original source files are always available for reuse, if a file becomes corrupted
Original Source Files
Source Files are “Added” to
the Project Folder
Supporting Files and Libraries
Easier to make projects portable
${PROJECT_ROOT} provides an anchor point for paths to files that travel with the project
Easier to maintain and update supporting files and libraries
Note: CCSv6 will automatically add ALL files contained in the folder where the project is created

## Slide 35: Lab1: Dual-Core Debug with F2837xD
Use Code Composer Studio (CCS) in dual-core debug environment
  Set up target configuration
  Create CPU1 project
    CPU1 blinks LED LD2 (software delay loop)
  Load and run CPU2 project
    CPU2 blinks LED LD3 (software delay loop)
LED LD2
LED LD3

## Slide 36: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 37: Reset Sources
POR – Power-on Reset generates a device reset during power-up conditions
RESC – Reset Cause register contains the cause of the last reset (sticky bits maintain state with multiple resets)
Note: Only F2807x devices support an on-chip voltage regulator (VREG) to generate the core voltage.
Watchdog Timer *
XRS pin active
To XRS pin
F28x7x
XRS
Power-on Reset
Hibernate Reset
Missing Clock Detect
Logic shown is functional representation, not actual implementation
* = CPU1.WD resets both cores and CPU2.WD resets CPU2 only
省電模式

## Slide 38: Dual-Core Boot Process
CPU1 starts execution from CPU1 boot ROM while CPU2 is held in reset
CPU1 controls the boot process
CPU2 goes through its own boot process under the control of CPU1 – except when CPU2 is set to boot-to-flash
IPC registers are used to communicate between CPU1 and CPU2 during the boot process

## Slide 39: Reset – Bootloader
TRST = JTAG Test Reset
EMU_BOOTCTRL register located in PIE RAM at 0x000D00
Z1OTP_BOOTCTRL register located in OTP at 0x07801E
Z2OTP_BOOTCTRL register located in OTP at 0x07821E
Reset vector fetched from boot ROM
0x3F FFC0
Emulation Boot
Boot determined by
EMU_BOOTCTRL:
EMU_KEY and EMU_BMODE
Stand-alone Boot
Boot determined by
2 GPIO pins and
ZxOTP_BOOTCTRL:
OTP_KEY and OTP_BMODE
TRST = 1
TRST = 0
Reset
ENPIE = 0
INTM = 1
YES
NO
Emulator Connected ?
CPU2
CPU2 held in reset until released by CPU1.

## Slide 40: Emulation Boot Mode (TRST = 1) slide 1 of 2
If either EMU_KEY or EMU_BMODE are invalid, the “wait” boot mode is used. These values can then be modified using the debugger and a reset issued to restart the boot process.
Emulation Boot
Boot determined by
EMU_BOOTCTRL :
EMU_KEY and EMU_BMODE
Emulator Connected
EMU_KEY = 0x5A ?
Boot Mode
Wait
NO
YES
EMU_BMODE = 0xFE ?
CPU1 only
YES
NO
EMU_BMODE = 0xFF ?
Boot Mode
Emulate CPU1/2 Stand-Alone
YES
NO
Boot Mode
Parallel I/O
SCI-A
Wait
GetMode
GPIO 72 GPIO 84
0 0
0 1
1 0
1 1
Boot pins can be mapped to any GPIO pins. GetMode reads ZxOTP_BOOTCTRL (not the boot pins).
Reads OTP for boot pins and boot mode.
EMU_BOOTPIN1
EMU_BOOTPIN0
EMU_BMODE
EMU_KEY
7 – 0
15 – 8
23 – 16
31 – 24
CPU1 EMU_BOOTCTRL Register
reserved
reserved
EMU_BMODE
EMU_KEY
7 – 0
15 – 8
23 – 16
31 – 24
CPU2 EMU_BOOTCTRL Register

## Slide 41: Emulation Boot Mode (TRST = 1) slide 2 of 2
Boot Mode
Parallel I/O
SCI-A
GetMode
SPI-A
I2C-A
CAN-A
M0 SARAM
FLASH
Wait
USB-0
SCI-A *
SPI-A *
I2C-A *
CAN-A *
EMU_BMODE =
0x00
0x01
0x03
0x04
0x05
0x07
0x0A
0x0B
other
0x0C
0x81
0x84
0x85
0x87
Boot Mode
FLASH
NO
Continued from previous slide
YES
OTP_KEY = 0x5A ?
Boot Mode
Parallel I/O
SCI-A
SPI-A
I2C-A
CAN-A
M0 SARAM
FLASH
USB-0
Wait
SCI-A *
SPI-A *
I2C-A *
CAN-A *
OTP_BMODE =
0x00
0x01
0x04
0x05
0x07
0x0A
0x0B
0x0C
other
0x81
0x84
0x85
0x87
* Alternate RX/TX GPIO pin mapping for CPU1 only
Boot Mode
FLASH
Wait
OTP_BMODE =
0x0B
other
CPU1 GetMode
CPU1 & CPU2
CPU2 GetMode
CPU1 only

## Slide 42: Stand-Alone Boot Mode (TRST = 0)
Stand-alone Boot
Boot determined by
2 GPIO pins and
ZxOTP_BOOTCTRL :
OTP_KEY and OTP_BMODE
Emulator Not Connected
Boot Mode
Parallel I/O
SCI
Wait
GetMode
GPIO GPIO
72 84
0 0
0 1
1 0
1 1
Boot Mode
FLASH
NO
Boot Mode
Parallel I/O
SCI-A
SPI-A
I2C-A
CAN-A
M0 SARAM
FLASH
USB-0
Wait
SCI-A *
SPI-A *
I2C-A *
CAN-A *
OTP_BMODE =
0x00
0x01
0x04
0x05
0x07
0x0A
0x0B
0x0C
other
0x81
0x84
0x85
0x87
Boot Mode
FLASH
Wait
OTP_BMODE =
0x0B
other
CPU1 GetMode
CPU2 GetMode
CPU1 only
Z1OTP_BOOTCTRL
OTP_KEY = 0x5A ?
Z2OTP_BOOTCTRL
OTP_KEY = 0x5A ?
NO
Use
Z1OTP_
BOOTCTRL
YES
YES
Use
Z2OTP_
BOOTCTRL
OTP_BOOTPIN1
OTP_BOOTPIN0
OTP_BMODE
OTP_KEY
7 – 0
15 – 8
23 – 16
31 – 24
CPU1 ZxOTP_BOOTCTRL Register
reserved
reserved
OTP_BMODE
OTP_KEY
7 – 0
15 – 8
23 – 16
31 – 24
CPU2 ZxOTP_BOOTCTRL Register

## Slide 43: Reset Code Flow - Summary
M0 SARAM (1Kw)
FLASH (512Kw)
0x3F7FF6
0x080000
0x000000
0x3F8000
0x3FFFC0
Boot ROM (32Kw)
BROM vector (64w)
* reset vector
Boot Code




RESET
Execution Entry
determined by
Emulation Boot Mode or
Stand-Alone Boot Mode
Bootloading
Routines
(SCI, SPI, I2C, USB, CAN, Parallel I/O)
InitBoot
0x000000
* reset vector = 0x3FEAC2 for CPU1; 0x3FE649 for CPU2

## Slide 44: Interrupt Sources
ePWM, eCAP, eQEP, ADC, SCI, SPI, I2C, eCAN, McBSP,
DMA, CLA, WD
Internal Sources
External Sources
XINT1 – XINT5
TZx
XRS
NMI
F28x CORE
INT1
INT13
INT2
INT3
INT12
INT14
XRS
•
•
•
TINT2
TINT1
TINT0
PIE
(Peripheral
Interrupt
Expansion)

## Slide 45: Maskable Interrupt Processing Conceptual Core Overview
A valid signal on a specific interrupt line causes the latch to display a “1” in the appropriate bit
1
0
1
(IFR)
“Latch”
Core
Interrupt
F28x
Core
(INTM)
“Global Switch”
(IER)
“Switch”
If the individual and global switches are turned “on” the interrupt reaches the core
INT1
INT2
INT14

## Slide 46: Core Interrupt Registers
RTOSINT
DLOGINT
INT14
INT13
INT12
INT11
INT10
INT9
8
9
10
11
12
13
14
15
INT8
INT7
INT6
INT5
INT4
INT3
INT2
INT1
0
1
2
3
4
5
6
7
Interrupt Flag Register (IFR)
RTOSINT
DLOGINT
INT14
INT13
INT12
INT11
INT10
INT9
8
9
10
11
12
13
14
15
INT8
INT7
INT6
INT5
INT4
INT3
INT2
INT1
0
1
2
3
4
5
6
7
Interrupt Enable Register (IER)
INTM
ST1
Bit 0
Interrupt Global Mask Bit (INTM)
(enable = 0 / disable = 1)
/*** Interrupt Enable Register ***/
extern cregister volatile unsigned int IER;
IER |= 0x0008; //enable INT4 in IER
IER &= 0xFFF7; //disable INT4 in IER
/*** Global Interrupts ***/
asm(“ CLRC INTM”); //enable global interrupts
asm(“ SETC INTM”); //disable global interrupts
(pending = 1 / absent = 0)
(enable = 1 / disable = 0)
產生interrupt

## Slide 47: Peripheral Interrupt Expansion - PIE
IFR
IER
INTM
28x
Core
Core Interrupt logic
PIE module for 192 Interrupts
INT1.y interrupt group
INT2.y interrupt group
INT3.y interrupt group
INT4.y interrupt group
INT5.y interrupt group
INT6.y interrupt group
INT7.y interrupt group
INT8.y interrupt group
INT9.y interrupt group
INT10.y interrupt group
INT11.y interrupt group
INT12.y interrupt group
INT1 – INT12
12 Interrupts
192
INT1.1
INT1.2
INT1.16
1
0
1
•
•
•
•
•
•
INT1
PIEIFR1
PIEIER1
Interrupt Group 1
(TINT1)
(TINT2)
INT13
INT14
NMI
Peripheral Interrupts 12 x 16 = 192

## Slide 48: F28377D PIE Assignment Table - Lower
INTx.8
INTx.7
INTx.6
INTx.5
INTx.4
INTx.3
INTx.2
INTx.1
INT1
WAKE
TINT0
ADCD1
XINT2
XINT1
ADCC1
ADCB1
ADCA1
INT2
PWM8_
TZ
PWM7_
TZ
PWM6_
TZ
PWM5_
TZ
PWM4_
TZ
PWM3_
TZ
PWM2_
TZ
PWM1_
TZ
INT3
PWM8
PWM7
PWM6
PWM5
PWM4
PWM3
PWM2
PWM1
INT4
ECAP6
ECAP5
ECAP4
ECAP3
ECAP2
ECAP1
INT5
EQEP3
EQEP2
EQEP1
INT6
MCBSP
B_TX
MCBSP
B_RX
MCBSP
A_TX
MCBSP
A_RX
SPIB_TX
SPIB_RX
SPIA_TX
SPIA_RX
INT7
DMA_CH6
DMA_CH5
DMA_CH4
DMA_CH3
DMA_CH2
DMA_CH1
INT8
SCID_TX
SCID_RX
SCIC_TX
SCIC_RX
I2CB_
FIFO
I2CB
I2CA_
FIFO
I2CA
INT9
DCANB_2
DCANB_1
DCANA_2
DCANA_1
SCIB_TX
SCIB_RX
SCIA_TX
SCIA_RX
INT10
ADCB4
ADCB3
ADCB2
ADCB_
EVT
ADCA4
ADCA3
ADCA2
ADCA_
EVT
INT11
CLA1_8
CLA1_7
CLA1_6
CLA1_5
CLA1_4
CLA1_3
CLA1_2
CLA1_1
INT12
FPU_UF
FPU_OF
VCU
PBIST
XINT5
XINT4
XINT3

## Slide 49: F28377D PIE Assignment Table - Upper
INTx.16
INTx.15
INTx.14
INTx.13
INTx.12
INTx.11
INTx.10
INTx.9
INT1
IPC3
IPC2
IPC1
IPC0
INT2
PWM12_
TZ
PWM11_
TZ
PWM10_
TZ
PWM9_
TZ
INT3
EPWM12
EPWM11
EPWM10
EPWM9
INT4
INT5
SD2
SD1
INT6
SPIC_TX
SPIC_RX
INT7
INT8
UPPA
INT9
USBA
INT10
ADCD4
ADCD3
ADCD2
ADCD_
EVT
ADCC4
ADCC3
ADCC2
ADCC_
EVT
INT11
INT12
CLA_UF
CLA_OF
AUX_PLL
_SLIP
SYS_PLL
_SLIP
RAM_ACC
_VIOLAT
FLASH_C
_ERROR
RAM_C_
ERROR
EMIF_
ERROR

## Slide 50: PIE Registers
PIEVECT
ENPIE
PIECTRL register
0
15 - 1
#include “F2837x_Device.h”
PieCtrlRegs.PIEIFR1.bit.INTx4 = 1; //manually set IFR for XINT1 in PIE group 1
PieCtrlRegs.PIEIER3.bit.INTx2 = 1; //enable PWM2INT in PIE group 3
PieCtrlRegs.PIEACK.all = 0x0004; //acknowledge the PIE group 3
PieCtrlRegs.PIECTRL.bit.ENPIE = 1; //enable the PIE
PIEIFRx register (x = 1 to 12)
INTx.16
INTx.15
INTx.14
INTx.13
INTx.12
INTx.11
INTx.10
INTx.9
INTx.8
INTx.7
INTx.6
INTx.5
INTx.4
INTx.3
INTx.2
INTx.1
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
PIEIERx register (x = 1 to 12)
INTx.16
INTx.15
INTx.14
INTx.13
INTx.12
INTx.11
INTx.10
INTx.9
INTx.8
INTx.7
INTx.6
INTx.5
INTx.4
INTx.3
INTx.2
INTx.1
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
reserved
PIEACKx
PIE Interrupt Acknowledge Register (PIEACK)
15 - 12
11
10
9
8
7
6
5
4
3
2
1
0
由指令產生interrupt

## Slide 51: PIE Block Initialization
•
•
•
// CPU Initialization
InitPieCtrl();
•
•
•
Main.c
•
•
•
// Initialize PIE_RAM
memcpy( );
•
•
•
PieCtrl.c
// Enable PIE Block
PieCtrlRegs.
PIECTRL.bit.
ENPIE=1;
•
•
•
•
•
•
// Base Vectors
PieVect.c
PIE_VECT_TABLE
•
•
•
// Core INT1 re-map
// Core INT12 re-map
PIE RAM
Vectors
512w
(ENPIE = 1)
Boot ROM
Reset Vector
1
2
2
3
Memory Map

## Slide 52: PIE Initialization Code Flow - Summary
RESET
<0x3F FFC0>
Reset Vector
<reset vector> = Boot Code
Flash Entry Point
<0x08 0000> = LB _c_int00
M0SARAM Entry Point
<0x00 0000> = LB _c_int00
_c_int00:
CALL main()
•
•
•
OR
main()
{ initialization();
}
Initialization()
{
Load PIE Vectors
Enable the PIE
Enable PIEIER
Enable Core IER
Enable INTM
}
PIE Vector Table
512 Word RAM
0x00 0D00 – 0EFF
•
•
•
Main.c
CodeStartBranch.asm
rts2800_fpu32.lib
Boot option determines code execution entry point
interrupt void name(void)
{
}
•
•
•
DefaultIsr.c
Interrupt
.sect “codestart”

## Slide 53: Interrupt Signal Flow – Summary
Peripheral
Interrupt
PIEIFRx
PIEIERx
INTx.y
PieCtrlRegs.PIEIERx.bit.INTxy = 1;
IER
INTM
IFR
asm(“ CLRC INTM”);
IER |= 0x0001;
 0x0FFF;
1
1
Peripheral Interrupt Expansion (PIE) – Interrupt Group x
Core Interrupt Logic
PIE Vector Table
INTx.y  name
interrupt void name(void)
{
}
•
•
•
DefaultIsr.c
Core
INTx
(For peripheral interrupts where x = 1 to 12, and y = 1 to 16)

## Slide 54: F2837xD Dual-Core Interrupt Structure
ePWM, eCAP, eQEP,
ADC, SCI, SPI, I2C,
eCAN, McBSP, WD
Internal Sources
External Sources
TZx
XRS
NMI
CPU1 CORE
INT1
INT13
INT2
INT3
INT12
INT14
•
•
•
ePIE.1
TINT2.1
TINT1.1
TINT0.1
XINT1 – XINT5
DMA1.1 CLA1.1
TINT0.2
TINT1.2
TINT2.2
Internal Sources
NMI
CPU2 CORE
INT1
INT13
INT2
INT3
INT12
INT14
•
•
•
IPC
ePIE.2
DMA1.2 CLA1.2

## Slide 55: F28x7x Oscillator / PLL Clock Module
* default
X2
XTAL OSC
X1
XTAL
XCLKIN
(X2 n.c.)
Internal
OSC 1
(10 MHz)
Internal
OSC 2
(10 MHz)
OSCCLKSRCSEL
110
101
101
011
010
001
000*
PLL
PLLCLK
OSCCLK
PLLSYSCLK
(PLL bypass)
SYSPLLMULT
MUX
1/n
SYSCLKDIV
OSC1CLK
OSC2CLK
EXTCLK
WDCLK
XCLKOUT
(GPIO 73)
1x
00*
01
1/n
AUXPLLCLK
XCLKOUTDIV
XCLKOUTSEL
CPU2.SYSCLK
CPU1.SYSCLK
PLLCLK
PLLSYSCLK
AUX
PLL
1/n
AUXPLLCLK
AUXOSCCLKSRCSEL
AUXPLLDIV
00*
01
10
AUXCLKIN (from GPIO)
AUXCLK

## Slide 56: F28x7x PLL and LOSPCP
IMULT CLKIN
0 0 0 0 0 0 0 OSCCLK / n * (PLL bypass)
0 0 0 0 0 0 1 OSCCLK x 1 / n
0 0 0 0 0 1 0 OSCCLK x 2 / n
0 0 0 0 0 1 1 OSCCLK x 3 / n
1 1 1 1 1 0 1 OSCCLK x 125/ n
1 1 1 1 1 1 0 OSCCLK x 126 / n
1 1 1 1 1 1 1 OSCCLK x 127 / n
PLL
PLLCLK
OSCCLK
CPUx
PLLSYSCLK
CPUx.SYSCLK
LOSPCP
(PLL bypass)
CPUx.LSPCLK
MUX
1/n
ClkCfgRegs.SYSPLLMULT.bit.IMULT
ClkCfgRegs.SYSCLKDIVSEL.bit.PLLSYSCLKDIV
ClkCfgRegs.LOSPCP.bit.LSPCLK
LSPCLK Peripheral Clk Freq
0 0 0 CPUx.SYSCLK / 1
0 0 1 CPUx.SYSCLK / 2
0 1 0 CPUx.SYSCLK / 4 *
0 1 1 CPUx.SYSCLK / 6
1 0 0 CPUx.SYSCLK / 8
1 0 1 CPUx.SYSCLK / 10
1 1 0 CPUx.SYSCLK / 12
1 1 1 CPUx.SYSCLK / 14
LSBs in reg. – others reserved
* default
SYSPLL
DIVSEL n
111111 /126
000010 /4 *
000001 /2
000000 /1
•
•
•
•
•
•
FMULT CLKIN
0 0 Fractional x 0 *
0 1 Fractional x 0.25
1 0 Fractional x 0.5
1 1 Fractional x 0.75
•
•
•
•
•
•
ClkCfgRegs.SYSPLLMULT.bit.FMULT

## Slide 57: F2837xD Dual-Core System Clock
WDCLK
WD.2
WD.1
PLLSYSCLK
CPUSELy
SCIx
CPU2.SYSCLK
CPU1.SYSCLK
SPIx
PERx
CPU2
CPU1
LOSPCP
LOSPCP
CPU2.LSPCLK
CPU1.LSPCLK
PERCLKDIVSEL
/1, /2
EPWM
EPWMCLK
CPUTIMER2.2
CPUTIMER2.1
CPU1.SYSCLK
INTOSC1
INTOSC2
EXTCLK
AUXPLLCLK
CPU2.SYSCLK
INTOSC1
INTOSC2
EXTCLK
AUXPLLCLK
CPU2.TMR2CLKCTL
CPU1.TMR2CLKCTL
LSPCLKDIV
PERx
EPWMCLKDIV
PERx.SYSCLK
PERx.SYSCLK
PERx.SYSCLK
EXTCLK
AUXCLKIN
CANxBCLKSEL
CANx Bit CLK

## Slide 58: Watchdog Timer Module
WDCLK
System
Reset
8-bit Watchdog
Counter
CLR
Watchdog
Reset Key
Register
55 + AA
Detector
1 0 1
/
/
3
3
WDDIS
WDCHK
Bad WDCHK Key
/512
Output
Pulse
WDRST
WDINT
WDOVERRIDE
Good Key
Watchdog
Prescaler
WDPS
WDCNTR
window minimum
WDWCR
WDCNTR less than WDWCR
CNT
WDKEY

## Slide 59: F28x7x GPIO Grouping Overview
Internal Bus
GPIO Port A Group
Mux1 Register
(GPAGMUX1)
[GPIO 0 to 15]
GPIO Port A
Direction Register
(GPADIR)
[GPIO 0 to 31]
GPIO Port A Mux1
Register
(GPAMUX1)
[GPIO 0 to 15]
GPIO Port A Group
Mux2 Register
(GPAGMUX2)
[GPIO 16 to 31]
GPIO Port A Mux2
Register
(GPAMUX2)
[GPIO 16 to 31]
GPIO Port A
Input
Qual
GPIO Port F Group
Mux1 Register
(GPFGMUX1)
[GPIO 160 to 175]
GPIO Port F
Direction Register
(GPFDIR)
[GPIO 160 to 191]
GPIO Port F Mux1
Register
(GPFMUX1)
[GPIO 160 to 175]
GPIO Port F Group
Mux2 Register
(GPFGMUX2)
[GPIO 176 to 191]
GPIO Port F Mux2
Register
(GPFMUX2)
[GPIO 176 to 191]
GPIO Port F
Input
Qual

## Slide 60: F28x7x GPIO Pin Block Diagram
See device datasheet for pin function selection matrices
•
•
01
00
•
•
10
11
Peripheral 1
Peripheral 2
Peripheral 3
•
•
01
00
•
•
10
11
Peripheral 5
Peripheral 6
Peripheral 7
•
•
01
00
•
•
10
11
Peripheral 9
Peripheral 10
Peripheral 11
•
•
01
00
•
•
10
11
Peripheral 13
Peripheral 14
Peripheral 15
•
•
10
11
•
•
01
00
0
4
8
12
Pin
Internal Pull-Up
0 = enable
(default GPIO 12-xx)
1 = disable
(default GPIO 0-11)
GPxPUD
0*
1
0 = Input
1 = Output
GPxSET
GPxCLEAR
GPxTOGGLE
GPxDAT
In
Out
GPxDIR
Input
Qualification
GPxINV
GPxQSEL1/2
GPxCTRL
GPxMUX1/2
GPxGMUX1/2
* = Default x = A, B, C, D, E, or F
Logic shown is functional representation, not actual implementation
To Input X-Bar
Output X-Bar muxed with Peripheral GPIO pins

## Slide 61: F28x7x GPIO Input Qualification
Qualification available on ports A - F
Individually selectable per pin
  no qualification (peripherals only)
  sync to CPUx.SYSCLK only
  qualify 3 samples
  qualify 6 samples
Input
Qualification
pin
to GPIO and peripheral modules
CPUx.SYSCLK
T
T
T
samples taken
T = qual period

## Slide 62: F28x7x GPIO Input X-Bar

## Slide 63: F28x7x GPIO Input X-Bar Architecture
Input | Destinations
INPUT1 | EPWM[TZ1], EPWM[TRIP1], EPWM X-Bar, Output X-Bar
INPUT2 | EPWM[TZ2], EPWM[TRIP2], EPWM X-Bar, Output X-Bar
INPUT3 | EPWM[TZ3], EPWM[TRIP3], EPWM X-Bar, Output X-Bar
INPUT4 | ADC, EPWM X-Bar, Output X-Bar, XINT1
INPUT5 | EXTSYNCIN1, EPWM X-Bar, Output X-Bar, XINT2
INPUT6 | EXTSYNCIN2, EPWM[TRIP6], EPWM X-Bar, Output X-Bar, XINT3
INPUT7 | ECAP1
INPUT8 | ECAP2
INPUT9 | ECAP3
INPUT10 | ECAP4
INPUT11 | ECAP5
INPUT12 | ECAP6
INPUT13 | XINT4
INPUT14 | XINT5
INPUTx
INPUTxSELECT
GPIO 0
GPIO n
This block diagram is replicated 14 times

## Slide 64: F28x7x GPIO Output X-Bar
EPWM/ECAP sync
ADCSOCAO
ADCSOCBO
ECAP1
ECAP2
ECAP3
ECAP4
ECAP5
ECAP6
ADCA
ADCB
ADCC
ADCD
GPIO
Module
CMPSS1
CMPSS8
INPUT X-Bar
OUTPUT
X-Bar
SD1
SD2
OUTPUT1
OUTPUT2
OUTPUT3
OUTPUT4
OUTPUT5
OUTPUT6
OUTPUT7
OUTPUT8
INPUT1
INPUT2
INPUT3
INPUT4
INPUT5
INPUT6
EVT1 to EVT4
EVT1 to EVT4
EVT1 to EVT4
EVT1 to EVT4
ECAP1.OUT
ECAP2.OUT
ECAP3.OUT
ECAP4.OUT
ECAP5.OUT
ECAP6.OUT
ADCSOCA
ADCSOCB
EXTSYNCOUT
CTRIPOUTH
CTRIPOUTL
CTRIPOUTL
CTRIPOUTH
FLT1.COMPH
FLT1.COMPL
FLT4.COMPH
FLT4.COMPL
FLT1.COMPH
FLT1.COMPL
FLT4.COMPH
FLT4.COMPL

## Slide 65: F28x7x GPIO Output X-Bar Architecture
MUX | 0 | 1 | 2 | 3
16 | SD1FLT1.COMPH | SD1FLT1.COMPH_OR_COMPL |  | 
17 | SD1FLT1.COMPL |  |  | 
18 | SD1FLT2.COMPH | SD1FLT2.COMPH_OR_COMPL |  | 
19 | SD1FLT2.COMPL |  |  | 
20 | SD1FLT3.COMPH | SD1FLT3.COMPH_OR_COMPL |  | 
21 | SD1FLT3.COMPL |  |  | 
22 | SD1FLT4.COMPH | SD1FLT4.COMPH_OR_COMPL |  | 
23 | SD1FLT4.COMPL |  |  | 
24 | SD2FLT1.COMPH | SD2FLT1.COMPH_OR_COMPL |  | 
25 | SD2FLT1.COMPL |  |  | 
26 | SD2FLT2.COMPH | SD2FLT2.COMPH_OR_COMPL |  | 
27 | SD2FLT2.COMPL |  |  | 
28 | SD2FLT3.COMPH | SD2FLT3.COMPH_OR_COMPL |  | 
29 | SD2FLT3.COMPL |  |  | 
30 | SD2FLT4.COMPH | SD2FLT4.COMPH_OR_COMPL |  | 
31 | SD2FLT4.COMPL |  |  | 
MUX | 0 | 1 | 2 | 3
0 | CMPSS1.CTRIPOUTH | CMPSS1.CTRIPH_OR_CTRIPL | ADCAEVT1 | ECAP1.OUT
1 | CMPSS1.CTRIPOUTL | INPUTXBAR1 |  | ADCCEVT1
2 | CMPSS2.CTRIPOUTH | CMPSS2.CTRIPH_OR_CTRIPL | ADCAEVT2 | ECAP2.OUT
3 | CMPSS2.CTRIPOUTL | INPUTXBAR2 |  | ADCCEVT2
4 | CMPSS3.CTRIPOUTH | CMPSS3.CTRIPH_OR_CTRIPL | ADCAEVT3 | ECAP3.OUT
5 | CMPSS3.CTRIPOUTL | INPUTXBAR3 |  | ADCCEVT3
6 | CMPSS4.CTRIPOUTH | CMPSS4.CTRIPH_OR_CTRIPL | ADCAEVT4 | ECAP4.OUT
7 | CMPSS4.CTRIPOUTL | INPUTXBAR4 |  | ADCCEVT4
8 | CMPSS5.CTRIPOUTH | CMPSS5.CTRIPH_OR_CTRIPL | ADCBEVT1 | ECAP5.OUT
9 | CMPSS5.CTRIPOUTL | INPUTXBAR5 |  | ADCDEVT1
10 | CMPSS6.CTRIPOUTH | CMPSS6.CTRIPH_OR_CTRIPL | ADCBEVT2 | ECAP6.OUT
11 | CMPSS6.CTRIPOUTL | INPUTXBAR6 |  | ADCDEVT2
12 | CMPSS7.CTRIPOUTH | CMPSS7.CTRIPH_OR_CTRIPL | ADCBEVT3 | 
13 | CMPSS7.CTRIPOUTL | ADCSOCA |  | ADCDEVT3
14 | CMPSS8.CTRIPOUTH | CMPSS8.CTRIPH_OR_CTRIPL | ADCBEVT4 | EXTSYNCOUT
15 | CMPSS8.CTRIPOUTL | ADCSOCB |  | ADCDEVT4
0
0.1
0.2
0.3
0.4
1
1.1
1.2
1.3
1.4
31
31.1
31.2
31.3
31.4
Latch
OUTPUTx
OUTPUTINV
OUTPUTLATCHENABLE
OUTPUTxMUXENABLE
OUTPUTxMUX0TO15CFG.MUX0
OUTPUTxMUX0TO15CFG.MUX1
OUTPUTxMUX16TO31CFG.MUX31
This block diagram is replicated 8 times
Muxed with Peripheral GPIO Pins

## Slide 66: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 67: Analog Subsystem
Four dual-mode ADCs
  16-bit mode
    1 MSPS each (up to 4 MSPS system)
    Differential inputs
    External reference
  12-bit mode
    3.5 MSPS each (up to 14 MSPS system)
    Single-ended or differential inputs
    Internal or external reference
Eight comparator subsystems
  Each contains:
    Two 12-bit reference DACs
    Two comparators
    Digital glitch filter
Three 12-bit buffered DAC outputs
Sigma-Delta Filter Module (SDFM)

## Slide 68: Analog Subsystem
ADC input models

## Slide 69: ADC Subsystem
*** Multiple ADC modules allow simultaneous sampling or independent operation ***

## Slide 70: ADC Module Block Diagram
12/16-bit
A/D
Converter
SOCx
EOCx
S/H
MUX
ADCRESULT0
ADCRESULT1
ADCRESULT2
ADCRESULT15
Result
MUX
ADC
Generation
Logic
ADC full-scale input range is 0 to 3.3V
CHSEL
ADC
Interrupt
Logic
ADCINT1-4
Software
External Pin(GPIO/ADCEXTSOC)
EPWMxSOCA/C (x = 1 to 12)
EPWMxSOCB/D (x = 1 to 12)
CPU1 Timer (0,1,2)
SOCx Signal
ADCINT1
ADCINT2
SOC0 TRIGSEL CHSEL ACQPS
SOC1 TRIGSEL CHSEL ACQPS
SOC2 TRIGSEL CHSEL ACQPS
SOC3 TRIGSEL CHSEL ACQPS
SOC15 TRIGSEL CHSEL ACQPS
SOCx Triggers
SOCx Configuration Registers
Post Processing Block
ADCIN1
ADCIN0
ADCIN2
ADCIN3
ADCIN14
ADCIN15
CPU2 Timer (0,1,2)

## Slide 71: ADC SOCx Functional Diagram
This block diagram is replicated 16 times
ADCINT1
ADCINT2
Re-Trigger
ADCINT1
ADCINT2
ADCINT3
ADCINT4
Channel
Select
Sample
Window
Result
Register
S
O
C
x
E
O
C
x
ADCSOCxCTL
ADCINTSOCSEL1
ADCINTSOCSEL2
INTSELxNy
ADCRESULTx
Software Trigger
TINT0 (CPU1 Timer 0)
TINT1 (CPU1 Timer 1)
TINT2 (CPU1 Timer 2)
ADCEXTSOC (GPIO)
SOCA/C (ePWM1)
SOCB/D (ePWM1)
SOCA/C (ePWM12)
SOCB/D (ePWM12)
TINT0 (CPU2 Timer 0)
TINT1 (CPU2 Timer 1)
TINT2 (CPU2 Timer 2)
T
r
i
g
g
e
r
ADCSOCFRC1

## Slide 72: ADC SOCx Functional Diagram

## Slide 73: Example – ADC Triggering
Sample A0  A2  A5 when ePWM1 SOCB/D is generated and then generate ADCINT1:
Channel
A0
Sample
7 cycles
Result0
Channel
A2
Sample
10 cycles
Result1
Channel
A5
Sample
8 cycles
Result2
SOC0
SOC1
SOC2
no interrupt
no interrupt
ADCINT1
SOCB/D (ETPWM1)
Sample A2  A4  A6 continuously and generate ADCINT2:
Channel
A2
Sample
10 cycles
Result3
Channel
A4
Sample
15 cycles
Result4
Channel
A6
Sample
12 cycles
Result5
SOC3
SOC4
SOC5
no interrupt
no interrupt
ADCINT2
ADCINT2
Software Trigger
Note: setting ADCINT2 flag does not need to generate an interrupt

## Slide 74: Example – ADC Ping-Pong Triggering
Sample all channels continuously and provide Ping-Pong interrupts to CPU/system:
Channel
B0
Sample
7 cycles
SOC0
no interrupt
ADCINT2
Software Trigger
Result0
Channel
B1
Sample
7cycles
SOC1
no interrupt
Result1
Channel
B2
Sample
7 cycles
SOC2
no interrupt
Result2
Channel
B3
Sample
7 cycles
SOC3
Result3
Channel
B4
Sample
7 cycles
SOC4
no interrupt
Result4
Channel
B5
Sample
7 cycles
SOC5
Result5
ADCINT1
ADCINT2
ADCINT1
Software Trigger

## Slide 75: ADC Conversion Priority
When multiple SOC flags are set at the same time – priority determines the order in which they are converted
High Priority
  High priority SOC will interrupt the round robin wheel after current conversion completes and insert itself as the next conversion
  After its conversion completes, the round robin wheel will continue where it was interrupted
Round Robin Burst Mode
  Allows a single trigger to convert one or more SOCs in the round robin wheel
  Uses BURSTTRIG instead of TRIGSEL for all round robin SOCs (not high priority)
Round Robin Priority (default)
  No SOC has an inherent higher priority than another
  Priority depends on the round robin pointer

## Slide 76: Conversion Priority Functional Diagram
Round Robin Pointer
Points to the last converted
round robin SOCx and
determines order
of conversions
SOC Priority
Determines cutoff point
for high priority and
round robin mode
SOC0
SOC1
SOC2
SOC3
SOC4
SOC5
SOC6
SOC7
SOC8
SOC9
SOC10
SOC11
SOC12
SOC13
SOC14
SOC15
Round Robin
High Priority
SOCPRIORITY
RRPOINTER
AdcRegs.SOCPRICTL

## Slide 77: Round Robin Burst Mode Diagram
Burst Enable
Disables/enables burst mode
BURSTEN
AdcxRegs.ADCBURSTCTL
BURSTSIZE
BURSTTRIGSEL
SOC Burst Size
Determines how many SOCs are converted per burst trigger
SOC Burst Trigger Source Select
Determines which trigger starts a burst conversion sequence
Software, CPU1 Timer0-2
ePWM1 ADCSOCA/C – B/D  ePWM12 ADCSOCA/C – B/D
CPU2 Timer0-2

## Slide 78: Purpose of the Post Processing Block
Offset Correction
  Remove an offset associated with an ADCIN channel possibly caused by external sensors and signal sources
    Zero-overhead; saving cycles
Error from Setpoint Calculation
  Subtract out a reference value which can be used to automatically calculate an error from a set-point or expected value
    Reduces the sample to output latency and software overhead
Limit and Zero-Crossing Detection
  Automatically perform a check against a high/low limit or zero-crossing and can generate a trip to the ePWM and/or an interrupt
    Decreases the sample to ePWM latency and reduces software overhead; trip the ePWM based on an out of range ADC conversion without CPU intervention
Trigger-to-Sample Delay Capture
  Capable of recording the delay between when the SOC is triggered and when it begins to be sampled
    Allows software techniques to reduce the delay error

## Slide 79: Post Processing Block - Diagram
補償因外部元件造成
的準位偏差
雙極性或誤差計算
Limit and zero-crossing detection
ADCEVTINTSEL
Register設定
ADC Event Status Register

## Slide 80: Post Processing Block Interrupt Event
Each ADC module contains four (4) Post Processing Blocks
Each Post Processing Block and be associated with any of the 16 ADCRESULTx registers

## Slide 81: Digital-to-Analog Converter
Three buffered 12-bit DACs
Provides a programmable reference output voltage
Capable of driving an external load
Ability to be synchronized with PWMSYNC events
Selectable reference voltage

## Slide 82: DAC Module
Ability to synchronize
with PWMSYNC
External
reference
DACREF
GND
Unipolar
output
voltage

## Slide 83: Buffered DAC Block Diagram
DACVALA * DACREF
4096
VDACOUT =
Ideal Output
VREFHIA can supply reference for DAC A and DAC B; VREFHIB can supply reference for DAC C
0
1
AMP
12-bit
DAC
DACVALS
DACREFSEL
VDAC
VREFHI
VSSA
VDDA
DACOUTEN
VDACOUT
DACVALA
0
1
DACREFSEL
VSSA
VREFLO

## Slide 84: Comparator Subsystem
Eight Comparator Subsystems (CMPSS)
Each CMPSS has:
  Two analog comparators
  Two programmable 12-bit DACs
  Two digital filters
  Ramp generator
Digital filter used to remove spurious trip signals (majority vote)
Ramp generator used peak current mode control
Ability to synchronize with PWMSYNC event

## Slide 85: Comparator Subsystem Block Diagram

## Slide 86: Comparator Subsystem Block Diagram
DACxVALA * DACREF
4096
VDACx =
DAC Reference
Comparator Truth Table
Voltages Output
Voltage A < Voltage B 0
Voltage A > Voltage B 1
+
COMPH
-
Digital Filter
12-bit
DAC
1
0
CTRIPH
0
1
CTRIPOUTH
DACHVALA
0
1
DACHVALS
+
COMPL
-
Digital Filter
12-bit
DAC
1
0
CTRIPL
0
1
CTRIPOUTL
DACLVALA
DACLVALS
ePWM
Event
Trigger
&
GPIO
MUX
CMPINxP
CMPINxN
COMPHINV
COMPLINV
COMPDACE
COMPHSOURCE
COMPLSOURCE
DACSOURCE

## Slide 87: Sigma Delta Filter Module (SDFM)
SDFM is a four-channel digital filter designed specifically for current measurement and resolver position decoding in motor control applications
Each channel can receive an independent modulator bit stream
Bit streams are processed by four individually programmable digital decimation filters
Filters include a fast comparator for immediate digital threshold comparisons for over-current monitoring
Filter-bypass mode available to enable data logging, analysis, and customized filtering

## Slide 88: SDFM Block Diagram

## Slide 89: Lab 2: Analog-to-Digital Converter
ADC
ADCINA0
RESULT0
...
data
memory
pointer rewind
CPU copies result
to buffer during
ADC ISR
ePWM2
ePWM2 triggering
ADC on period match using SOCA trigger every 20 µs (50 kHz)
DACB
Toggle
(GPIO8)
connector
wire
View ADC buffer PWM Samples
Code Composer
Studio

## Slide 90: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 91: ePWM Module Signals and Connections
ePWMx
ePWMx+1
EPWMxSYNCI
EPWMxSYNCO
PIE
CLA
EPWMxINT
EPWMxTZINT
ePWMx-1
EPWMxSOCB
EPWMxSOCA
ADC
ePWM
X-Bar
EMUSTOP – TZ6
CLOCKFAIL – TZ5
EQEPERR – TZ4
CPU
SYSCTRL
eQEP
EPWMxA
EPWMxB
GPIO
MUX
INPUT
X-Bar

## Slide 92: ePWM Block Diagram
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
TZ1-TZ3
INPUT X-Bar
ePWM X-Bar
EPWMCLK
Compare
Registers
Event Trigger
Compare
Registers

## Slide 93: ePWM Time-Base Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Compare
Registers
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 94: ePWM Time-Base Count Modes
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform

## Slide 95: ePWM Phase Synchronization
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=120°
Phase

EPWM2A
EPWM2B
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=240°
Phase

EPWM3A
EPWM3B
SyncIn
SyncOut
CTR=zero
CTR=CMPB *
X
En
o
o
o
o
o
o
o
=0°
Phase

EPWM1A
EPWM1B
=120°
=120°
=240°
Ext. SyncIn
To eCAP1
SyncIn
* Extended selection for CMPC and CMPD available

## Slide 96: ePWM Compare Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 97: ePWM Compare Event Waveforms
TBCTR
TBCTR
TBCTR
TBPRD
TBPRD
TBPRD
Count Up Mode
Count Down Mode
Count Up and Down Mode
Asymmetrical
Waveform
Asymmetrical
Waveform
Symmetrical
Waveform
CMPA
CMPA
CMPA
CMPB
CMPB
CMPB





















= compare events are fed to the Action Qualifier Sub-Module



















CMPC and CMPD available for use as event triggers

## Slide 98: ePWM Action Qualifier Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 99: ePWM Action Qualifier Actions for EPWMA and EPWMB
SW

SW

SW
X
SW
T
S/W
Force
Do Nothing
Clear Low
Set High
Toggle
EPWM
Output
Actions
Time-Base Counter equals:
Z

Z

Z
X
Z
T
Zero
CA

CA

CA
X
CA
T
CMPA
CB

CB

CB
X
CB
T
CMPB
P

P

P
X
P
T
TBPRD
T1

T1

T1
X
T1
T
T1
T2

T2

T2
X
T2
T
T2
Trigger Events:
Tx Event Sources = DCAEVT1, DCAEVT2, DCBEVT1, DCBEVT2, TZ1, TZ2, TZ3, EPWMxSYNCIN

## Slide 100: ePWM Count Up Asymmetric Waveform with Independent Modulation on EPWMA / B
Z

P
X
CB
X
CA

Z

P
X
CB
X
CA

Z

P
X
Z

P
X
CB

CA
X
Z

P
X
CB

CA
X
Z

P
X
TBCTR
TBPRD




EPWMA
EPWMB





CMPA
CMPB
Notes: The next few figures show how the action qualifier uses the compare matches to modulate the output pins. Notice that the output pins for EPWMA and EPWMB are completely independent. Here, on the EPWMA output, the waveform will be set high on zero match and clear low on compare A match. On the EPWMB output, the waveform will be set high on zero match and clear low on compare B match.

## Slide 101: ePWM Count Up Asymmetric Waveform with Independent Modulation on EPWMA
CA

CB

CA

CB

Z
T
Z
T
Z
T
EPWMA
EPWMB
TBCTR
TBPRD






CMPB
CMPA



Notes: This figure has the EPWMA output set high on compare A match and clear low on compare B match, while the EPWMB output is configured to toggle on zero match.

## Slide 102: ePWM Count Up-Down Symmetric Waveform with Independent Modulation on EPWMA / B
CA

CA

CA

CA

CB

CB

CB

CB

EPWMA
EPWMB
TBCTR
TBPRD










CMPB
CMPA



Notes: Here you can see that we can have different output actions on the up-count and down-count using a single compare register. So, for the EPWMA and EPWMB outputs, we are setting high on the compare A and B up-count matches and clearing low on the compare A and B down-down matches.

## Slide 103: ePWM Count Up-Down Symmetric Waveform with Independent Modulation on EPWMA
CA

CB

CA

CB

Z

P

Z

P

EPWMA
EPWMB
TBCTR
TBPRD






CMPB
CMPA



Notes: And finally, again using different output actions on the up-count and down-count, we have the EPWMA output set high on the compare A up-count match and clear low on the compare B down-count match. The EPWMB output will clear low on zero match and set high on period match.

## Slide 104: ePWM Dead-Band Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 105: Motivation for Dead-Band
to power switching device
supply rail
gate signals are
complementary PWM
Transistor gates turn on faster than they shut off
Short circuit if both gates are on at same time!

## Slide 106: ePWM Dead-Band Block Diagram
Rising Edge Delay
In Out
(14-bit counter)
Falling Edge Delay
In Out
(14-bit counter)



0
1



0
1



0
1



1
0






PWMxA
PWMxB
PWMxB
PWMxA
S1
S0
S2
S3
FED
RED
OUT-MODE
POLSEL



0
1



0
1
S4
S5
IN-MODE
HALFCYCLE



0
1



0
1
S6
S7
OUTSWAP




1
0
S8



0
1
S8
DEDB-
MODE



## Slide 107: ePWM Chopper Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 108: Purpose of the PWM Chopper
Allows a high frequency carrier signal to modulate the PWM waveform generated by the Action Qualifier and Dead-Band modules
Used with pulse transformer-based gate drivers to control power switching elements

## Slide 109: ePWM Chopper Waveform
EPWMxA
EPWMxB
CHPFREQ
EPWMxA
EPWMxB
OSHT
EPWMxA
Programmable
Pulse Width
(OSHTWTH)
Sustaining
Pulses
With One-Shot Pulse on EPWMxA and/or EPWMxB

## Slide 110: ePWM Trip-Zone and Digital Compare Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 111: Trip-Zone and Digital Compare Inputs
GPIO
MUX
INPUT
X-BAR
ePWM
X-BAR
Trip-
Zone
Sub-
Module
Digital
Compare
Sub-
Module
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN6
TRIPIN4
TRIPIN5
TRIPIN7
TRIPIN8
TRIPIN9
TRIPIN10
TRIPIN11
TRIPIN12
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN6
TRIPIN4
TRIPIN5
TRIPIN7
TRIPIN8
TRIPIN9
TRIPIN10
TRIPIN11
TRIPIN12
TZ4 TZ5 TZ6
TRIP COMBO
TRIPIN14
TRIPIN15
12
DCAHTRIPSEL
DCALTRIPSEL
DCBHTRIPSEL
DCBLTRIPSEL

## Slide 112: ePWM X-Bar
EPWM/ECAP sync
ADCSOCAO
ADCSOCBO
ECAP1
ECAP2
ECAP3
ECAP4
ECAP5
ECAP6
ADCA
ADCB
ADCC
ADCD
All
ePWM
Modules
CMPSS1
CMPSS8
INPUT X-Bar
ePWM
X-Bar
SD1
SD2
TRIPIN4
TRIPIN5
TRIPIN7
TRIPIN8
TRIPIN9
TRIPIN10
TRIPIN11
TRIPIN12
INPUT1
INPUT2
INPUT3
INPUT4
INPUT5
INPUT6
EVT1 to EVT4
EVT1 to EVT4
EVT1 to EVT4
EVT1 to EVT4
ECAP1.OUT
ECAP2.OUT
ECAP3.OUT
ECAP4.OUT
ECAP5.OUT
ECAP6.OUT
ADCSOCA
ADCSOCB
EXTSYNCOUT
CTRIPOUTH
CTRIPOUTL
CTRIPOUTL
CTRIPOUTH
FLT1.COMPH
FLT1.COMPL
FLT4.COMPH
FLT4.COMPL
FLT1.COMPH
FLT1.COMPL
FLT4.COMPH
FLT4.COMPL

## Slide 113: ePWM X-Bar Architecture
MUX | 0 | 1 | 2 | 3
16 | SD1FLT1.COMPH | SD1FLT1.COMPH_OR_COMPL |  | 
17 | SD1FLT1.COMPL |  |  | 
18 | SD1FLT2.COMPH | SD1FLT2.COMPH_OR_COMPL |  | 
19 | SD1FLT2.COMPL |  |  | 
20 | SD1FLT3.COMPH | SD1FLT3.COMPH_OR_COMPL |  | 
21 | SD1FLT3.COMPL |  |  | 
22 | SD1FLT4.COMPH | SD1FLT4.COMPH_OR_COMPL |  | 
23 | SD1FLT4.COMPL |  |  | 
24 | SD2FLT1.COMPH | SD2FLT1.COMPH_OR_COMPL |  | 
25 | SD2FLT1.COMPL |  |  | 
26 | SD2FLT2.COMPH | SD2FLT2.COMPH_OR_COMPL |  | 
27 | SD2FLT2.COMPL |  |  | 
28 | SD2FLT3.COMPH | SD2FLT3.COMPH_OR_COMPL |  | 
29 | SD2FLT3.COMPL |  |  | 
30 | SD2FLT4.COMPH | SD2FLT4.COMPH_OR_COMPL |  | 
31 | SD2FLT4.COMPL |  |  | 
MUX | 0 | 1 | 2 | 3
0 | CMPSS1.CTRIPOUTH | CMPSS1.CTRIPH_OR_CTRIPL | ADCAEVT1 | ECAP1.OUT
1 | CMPSS1.CTRIPOUTL | INPUTXBAR1 |  | ADCCEVT1
2 | CMPSS2.CTRIPOUTH | CMPSS2.CTRIPH_OR_CTRIPL | ADCAEVT2 | ECAP2.OUT
3 | CMPSS2.CTRIPOUTL | INPUTXBAR2 |  | ADCCEVT2
4 | CMPSS3.CTRIPOUTH | CMPSS3.CTRIPH_OR_CTRIPL | ADCAEVT3 | ECAP3.OUT
5 | CMPSS3.CTRIPOUTL | INPUTXBAR3 |  | ADCCEVT3
6 | CMPSS4.CTRIPOUTH | CMPSS4.CTRIPH_OR_CTRIPL | ADCAEVT4 | ECAP4.OUT
7 | CMPSS4.CTRIPOUTL | INPUTXBAR4 |  | ADCCEVT4
8 | CMPSS5.CTRIPOUTH | CMPSS5.CTRIPH_OR_CTRIPL | ADCBEVT1 | ECAP5.OUT
9 | CMPSS5.CTRIPOUTL | INPUTXBAR5 |  | ADCDEVT1
10 | CMPSS6.CTRIPOUTH | CMPSS6.CTRIPH_OR_CTRIPL | ADCBEVT2 | ECAP6.OUT
11 | CMPSS6.CTRIPOUTL | INPUTXBAR6 |  | ADCDEVT2
12 | CMPSS7.CTRIPOUTH | CMPSS7.CTRIPH_OR_CTRIPL | ADCBEVT3 | 
13 | CMPSS7.CTRIPOUTL | ADCSOCA |  | ADCDEVT3
14 | CMPSS8.CTRIPOUTH | CMPSS8.CTRIPH_OR_CTRIPL | ADCBEVT4 | EXTSYNCOUT
15 | CMPSS8.CTRIPOUTL | ADCSOCB |  | ADCDEVT4
0
0.1
0.2
0.3
0.4
1
1.1
1.2
1.3
1.4
31
31.1
31.2
31.3
31.4
TRIPINx
TRIPOUTPUTINV
TRIPxMUXENABLE
TRIPxMUX0TO15CFG.MUX0
TRIPxMUX0TO15CFG.MUX1
TRIPxMUX16TO31CFG.MUX31
This block diagram is replicated 8 times

## Slide 114: Trip-Zone Features
Trip-Zone has a fast, clock independent logic path to high-impedance the EPWMxA/B output pins
Interrupt latency may not protect hardware when responding to over current conditions or short-circuits through ISR software
Supports: #1) one-shot trip for major short circuits or over current conditions
#2) cycle-by-cycle trip for current limiting operation
CPU
core
P
W
M
O
U
T
P
U
T
S
EPWMxTZINT
TZ6
TZ5
TZ4
ePWM X-Bar
INPUT X-Bar
Cycle-by-Cycle
Mode
One-Shot
Mode
EPWMxA
EPWMxB
Digital
Compare
CPU
SYSCTRL
eQEP1
EMUSTOP
CLOCKFAIL
EQEP1ERR
Over
Current
Sensors

## Slide 115: Purpose of the Digital Compare Sub-Module
Generates ‘compare’ events that can:
  Trip the ePWM
  Generate a Trip interrupt
  Sync the ePWM
  Generate an ADC start of conversion
Digital compare module inputs are:
  Input X-Bar
  ePWM X-Bar
  Trip-zone input pins
A compare event is generated when one or more of its selected inputs are either high or low
Optional ‘Blanking’ can be used to temporarily disable the compare action in alignment with PWM switching to eliminate noise effects

## Slide 116: Digital Compare Sub-Module Signals
Digital Trip
Event A1
Compare
Digital Trip
Event A2
Compare
Digital Trip
Event B1
Compare
Digital Trip
Event B2
Compare
Generate PWM Sync
Time-Base Sub-Module
Generate SOCA
Event-Trigger Sub-Module
Trip PWMA Output
Generate Trip Interrupt
Trip-Zone Sub-Module
Generate PWM Sync
Time-Base Sub-Module
Generate SOCB
Event-Trigger Sub-Module
Trip PWMB Output
Generate Trip Interrupt
Trip-Zone Sub-Module
DCAH
DCAL
DCBH
DCBL
DCTRIPSEL
TZDCSEL
DCACTL / DCBCTL
DCAEVT1
DCAEVT2
DCBEVT1
DCBEVT2
blanking
blanking
TRIPIN1 & TZ1
TRIPIN2 & TZ2
TRIPIN3 & TZ3
TRIPIN4
TRIPIN12
TRIPIN15
TRIPIN14
TRIP COMBO
●
●
●

## Slide 117: Digital Compare Events
The user selects the input for each of DCAH, DCAL, DCBH, DCBL
Each A and B compare uses its corresponding DCyH/L inputs (y = A or B)
The user selects the signal state that triggers each compare from the following choices:
DCyH  low DCyL  don’t care
DCyH  high DCyL  don’t care
iii. DCyL  low DCyH  don’t care
iv. DCyL  high DCyH  don’t care
v. DCyL  high DCyH  low

## Slide 118: ePWM Event-Trigger Sub-Module
16-Bit
Time-Base
Counter
Compare
Logic
Action
Qualifier
Dead
Band
PWM
Chopper
Trip
Zone
Period
Register
Clock
Prescaler
EPWMxA
EPWMxB
TZy
EPWMxSYNCI
EPWMxSYNCO
TBCLK
Digital
Compare
Compare
Registers
Event Trigger
Compare
Registers
INPUT X-Bar
ePWM X-Bar
TZ1-TZ3
EPWMCLK

## Slide 119: ePWM Event-Trigger Interrupts and SOC
TBCTR
TBPRD
CMPD
CMPA
CTR = 0
CTR = PRD
CTRU = CMPA
CTRD = CMPA
CTRU = CMPB
CTRD = CMPB
CTR = 0 or PRD
CMPC
CMPB
CTRU = CMPC
CTRD = CMPC
CTRU = CMPD
CTRD = CMPD






















## Slide 120: Hi-Resolution PWM (HRPWM)
Significantly increases the resolution of conventionally derived digital PWM
Uses 8-bit extensions to Compare registers (CMPxHR), Period register (TBPRDHR) and Phase register (TBPHSHR) for edge positioning control
Typically used when PWM resolution falls below ~9-10 bits which occurs at frequencies greater than ~200 kHz (with system clock of 100 MHz)
Not all ePWM outputs support HRPWM feature (see device datasheet)
PWM Period
Device Clock
(i.e. 100 MHz)
Regular PWM Step
(i.e. 10 ns)
HRPWM
Micro Step (~150 ps)
HRPWM divides a clock cycle into smaller steps
called Micro Steps
(Step Size ~= 150 ps)
ms
ms
ms
ms
ms
ms
Calibration Logic
Calibration Logic tracks the number of Micro Steps per clock to account for variations caused by Temp/Volt/Process
(fixed Time-Base/2)

## Slide 121: Capture Module (eCAP)
The eCAP module timestamps transitions on a capture input pin
  Can be used to measure the time width of a pulse
Auxiliary PWM generation
Timer
Timestamp
Values
Trigger
pin
t1
t2

## Slide 122: eCAP Module Block Diagram – Capture Mode
32-Bit
Time-Stamp
Counter
Capture 1
Register
Event
Prescale
Polarity
Select 1
Polarity
Select 2
Polarity
Select 3
Polarity
Select 4
Capture 2
Register
Capture 3
Register
Capture 4
Register
Event Logic
ECAPx
pin
CAP1POL
CAP2POL
CAP3POL
CAP4POL
PRESCALE
CPUx.SYSCLK

## Slide 123: eCAP Module Block Diagram – APWM Mode
32-Bit
Time-Stamp
Counter
Period
Register
(CAP3)
Period
Register
(CAP1)
Compare
Register
(CAP4)
Compare
Register
(CAP2)
PWM
Compare
Logic
ECAP
pin
Shadowed
Shadowed
immediate
mode
shadow
mode
shadow
mode
immediate
mode
CPUx.SYSCLK

## Slide 124: What is an Incremental Quadrature Encoder?
A digital (angular) position sensor
slots spaced  deg. apart
photo sensors spaced /4 deg. apart
light source (LED)
shaft rotation
Ch. A
Ch. B
Quadrature Output from Photo Sensors

/4
Incremental Optical Encoder

## Slide 125: How is Position Determined from Quadrature Signals?
Ch. A
Ch. B
(00)
(11)
(10)
(01)
(A,B) =
00
01
11
10
Quadrature Decoder
State Machine
increment
counter
decrement
counter
Position resolution is /4 degrees
Illegal Transitions; generate phase error interrupt

## Slide 126: eQEP Module Block Diagram
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
Generate the direction and clock for the position counter in quadrature count mode
Generate a sync output and/or interrupt on a position compare match
Measure the elapsed time between the unit position events; used for low speed measurement
Generate periodic interrupts for velocity calculations
Monitors the quadrature clock to indicate proper operation of the motion control system
Quadrature -clock mode
Direction -count mode
CPUx.SYSCLK

## Slide 127: eQEP Module Connections
Ch. A
Ch. B
Index
Quadrature
Decoder
EQEPxA/XCLK
EQEPxB/XDIR
EQEPxI
EQEPxS
Position/Counter
Compare
Quadrature
Capture
32-Bit Unit
Time-Base
QEP
Watchdog
Strobe
from homing sensor
CPUx.SYSCLK

## Slide 128: Lab 3: Control Peripherals
ADCC
...
pointer rewind
CPU copies
results to
buffers during
ADC ISR
PWM2
connector
wire
ADCC3
Phase
TB Counter
Compare
Action Qualifier
PWM5A
View both ADC buffers
Code Composer
Studio
PWM2 triggering
ADC on period match using SOCA trigger every 20 µs (50 kHz)
ADCA
...
pointer rewind
connector
wire
ADCA0
TB Counter
Compare
Action Qualifier
PWM1A
RESULT0
RESULT0
AdcaResults
AdccResults
PWM1 period = programmable
PWM1 duty = programmable
PWM5 period = synchronized
PWM5 duty = programmable
PWM5 phase = programmable
SYNC
Notes: This foil describes the lab flow.
Connector wire: used to select the desired input to the ADC.
GP Timer 2: used to auto-trigger the ADC at a 50kHz rate.
The ADC will send an interrupt to the CPU when each conversion is done. Note that we are taking an ADC interrupt on every conversion (IM=0 in ADCTRL2), rather than on every other conversion. We could have written the code to do the later if we had wanted to, and saved some CPU interrupt overhead.
In the ADC ISR, the CPU will read the ADC result FIFO, and write the result into the data memory allocated for use as the results buffer. The CPU will then increment the pointer into the buffer, and check to see if the end of the buffer has been reached. If so, the pointer is rewound to the beginning of the buffer.
The contents of the buffer will be plotted in Code Explorer.

## Slide 129: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 130: IPC Device Features
Global Shared SARAM
Message SARAM
IPC Message Registers
IPC Interrupts and Flags
Clock Configuration Semaphore
Flash Pump Semaphore
Free Running Counter
Allows Communications Between the Two CPU Subsystems

## Slide 131: IPC Global Shared SARAM
Up to 16 Blocks (GS0 – GS15)
4K words each Block
  Can be configured to be used by CPU1 or CPU2
  Typically used by the application
  Also can be used to pass messages
Ownership | CPU1 Subsystem |  | CPU2 Subsystem | 
 | CPU1 | CPU1.DMA | CPU2 | CPU2.DMA
CPU1 Subsystem* | R/W/Exe | R/W | R | R
CPU2 Subsystem | R | R | R/W/Exe | R/W
* default

## Slide 132: IPC Message SARAM
2 Blocks
1K words each Block
  Used to pass messages or data between CPU1 and CPU2
  Always enabled – configuration is fixed
Message RAM | CPU1 Subsystem |  | CPU2 Subsystem | 
 | CPU1 | CPU1.DMA | CPU2 | CPU2.DMA
CPU1 to CPU2 (“C1toC2”) | R/W | R/W | R | R
CPU2 to CPU1 (“C2toC1”) | R | R | R/W | R/W

## Slide 133: IPC Message Registers
Provides very simple and flexible messaging
Dedicated registers mapped to both CPU’s
The definition (what the register content means) is up to the application software
TI’s IPC-Lite drivers use the IPC message registers
Local Register Name | Local CPU | Remote CPU | Remote Register Name
IPCSENDCOM | R/W | R | IPCRECVCOM
IPCSENDADDR | R/W | R | IPCRECVADDR
IPCSENDDATA | R/W | R | IPCRECVDATA
IPCREMOTEREPLY | R | R/W | IPCLOCALREPLY

## Slide 134: IPC Interrupts and Flags
CPU1 to CPU2: 32 flags with 4 interrupts
CPU2 to CPU1: 32 flags with 4 interrupts
Register | 
IPCSET | Message waiting (send interrupt and/or set flag)
IPCFLG | Bit is set by the “SET” register
IPCCLR | Clear the flag
Requesting CPU Set, Flag and Clear registers
Register | 
IPCSTS | Status (reflects the FLG bit)
IPCACK | Clear STS and FLG
Receiving CPU  Status and Acknowledge registers
Prefix indicates request and receive CPU:
C1TOC2IPCSET / C2TOC1IPCSET

## Slide 135: Messaging with IPC Flags and Interrupts

## Slide 136: Basic IPC Data Transfer
Basic option – no software drivers needed and easy to use!
  Use the message SARAM’s and global shared SARAM’s (GSx blocks) to pass data between processors at a known address
  Use the IPC flag registers to tell the other processor that the data is ready
C1toC2 MSG RAM
C2toC1 MSG RAM
GSx Shared SARAM’s
CPU1 Application
CPU2 Application
Message
1: Write a message to C1toC2 MSG RAM
C1TOC2IPCFLG
C1TOC2IPCSTS
2: Write 1 to C1TOC2IPCSET bit
3: sees C1TOC2IPCSTS bit is set
4: read message
5: write 1 to C1TOC2IPCACK bit

## Slide 137: IPC Software Solutions Summary
Basic Option
  No software drivers needed
  Uses IPC registers only (simple message passing)
IPC-Lite Software API Driver
  Uses IPC registers only (no memory used)
  Limited to 1 IPC interrupt at a time
  Limited to 1 command/message at a time
  CPU1 can use IPC-Lite to communicate with CPU2 boot ROM
Main IPC Software API Driver
  Uses circular buffers message RAMs
  Can queue up to 4 messages prior to processing (configurable)
  Can use multiple IPC ISRs at a time
  Requires additional setup in application code prior to use

## Slide 138: Lab 4: Inter-Processor Communications
...
pointer rewind
View ADC buffer
Code Composer
Studio
PWM2 triggers
ADCA at 50 kHz
...
pointer rewind
connector
wire
IPC2
IPC1
Sine Table
Adc Results
RESULT0
ADC-A
Pin 11
DACVALS
DAC-B
IPC2 receive ISR
Reads IPC2 data and stores in circular buffer
Writes next sine data to IPC1
CPU1
CPU2
IPC1 receive ISR
Reads IPC1 data and writes into DAC-B
ADCA EOC ISR
Reads ADC result and writes to IPC2
Pin 09
IPCRECVADDR
IPCSENDDATA
IPCSENDADDR
IPCRECVDATA
Notes: This foil describes the lab flow.
Connector wire: used to select the desired input to the ADC.
GP Timer 2: used to auto-trigger the ADC at a 50kHz rate.
The ADC will send an interrupt to the CPU when each conversion is done. Note that we are taking an ADC interrupt on every conversion (IM=0 in ADCTRL2), rather than on every other conversion. We could have written the code to do the later if we had wanted to, and saved some CPU interrupt overhead.
In the ADC ISR, the CPU will read the ADC result FIFO, and write the result into the data memory allocated for use as the results buffer. The CPU will then increment the pointer into the buffer, and check to see if the end of the buffer has been reached. If so, the pointer is rewound to the beginning of the buffer.
The contents of the buffer will be plotted in Code Explorer.

## Slide 139: Outline
Workshop Introduction
Architectural Overview
Programming Development Environment
  Lab 1: Using Code Composer Studio with the F2837xD
Reset, Interrupts and System Initialization
Analog Subsystem
  Lab 2: Configuring the ADC as a data acquisition system
Control Peripherals
  Lab 3: Generating a PWM waveform
Inter-Processor Communications (IPC)
  Lab 4: Data transfer using Inter-Processor Communications
Support Resources

## Slide 140: C2000 MCU Multi-day Training Course
TMS320F2806x Workshop Outline
- Architectural Overview
- Programming Development Environment
- Peripheral Register Header Files
- Reset and Interrupts
- System Initialization
- Analog-to-Digital Converter
- Control Peripherals
- Numerical Concepts
- Direct Memory Access (DMA)
- Control Law Accelerator (CLA)
- Viterbi, Complex Math, CRC Unit (VCU)
- System Design
- Communications
- Support Resources
In-depth hands-on TMS320F28069 Design and Peripheral Training

## Slide 141: controlSUITE™

## Slide 142: C2000 Experimenter’s Kit F28069, F28035, F28027, F28335, F2808, C28343, C28346, F28M35, F28377D
Experimenter Kits include
  controlCARD
  USB docking station
  C2000 Applications Software CD with example code and full hardware details
  Code Composer Studio
Docking station features
  Access to controlCARD signals
  Breadboard areas
  Onboard USB JTAG Emulation
    JTAG emulator not required
Available through TI authorized distributors and the TI eStore
Part Number:
  TMDSDOCK28069
  TMDSDOCK28035
  TMDSDOCK28027
  TMDSDOCK28335
  TMDSDOCK2808
  TMDSDOCKH52C1
  TMDSDOCK28377D
  JTAG emulator required for:
  TMDSDOCK28343
  TMDSDOCK28346-168

## Slide 143: F28335 Peripheral Explorer Kit
Experimenter Kit includes
  F28335 controlCARD
  Peripheral Explorer baseboard
  C2000 Applications Software CD with example code and full hardware details
  Code Composer Studio
Peripheral Explorer features
  ADC input variable resistors
  GPIO hex encoder & push buttons
  eCAP infrared sensor
  GPIO LEDs, I2C & CAN connection
  Analog I/O (AIC+McBSP)
  Onboard USB JTAG Emulation
  JTAG emulator not required
Available through TI authorized distributors and the TI eStore
TMDSPREX28335

## Slide 144: C2000 controlSTICK Evaluation Tool F28069, F28027
Low-cost USB evaluation tool
Onboard JTAG Emulation
  JTAG emulator not required
Access to controlSTICK signals
C2000 Applications Software CD with example code and full hardware details
Code Composer Studio
Available through TI authorized distributors and the TI eStore
Part Number:
  TMDX28069USB
  TMDS28027USB

## Slide 145: C2000 LaunchPad Evaluation Kit F28027, F28027F, F28069M, F28075
Low-cost evaluation kit
  F28027 and F28075 standard version
  F28027F version with InstaSPIN-FOC
  F28069M version with InstaSPIN-MOTION
Various BoosterPacks available
Onboard JTAG Emulation
  JTAG emulator not required
Access to LaunchPad signals
C2000 Applications Software with example code and full hardware details in available in controlSUITE
Code Composer Studio
Available through TI authorized distributors and the TI eStore
Part Number:
  LAUNCHXL-F28027
  LAUNCHXL-F28027F
  LAUNCHXL-F28069M
  LAUNCHXL-F28075

## Slide 146: C2000 controlCARD Application Kits
Developer’s Kit for – Motor Control, PFC, High Voltage, Digital Power, Renewable Energy, LED Lighting, etc.
Kits includes
  controlCARD and application specific baseboard
  Code Composer Studio
Software download includes
  Complete schematics, BOM, gerber files, and source code for board and all software
  Quick-start demonstration GUI for quick and easy access to all board features
  Fully documented software specific to each kit and application
See www.ti.com/c2000 for other kits and more details
Available through TI authorized distributors and the TI eStore

## Slide 147: XDS100 / XDS200 Class JTAG Emulators
Blackhawk
  USB100v2
Blackhawk
  USB200
Spectrum Digital
  XDS200
www.blackhawk-dsp.com
www.spectrumdigital.com
Spectrum Digital
  XDS100v2

## Slide 148: C2000 Workshop Download Wiki
http://www.ti.com/hands-on-training

## Slide 149: For More Information . . .
USA – Product Information Center (PIC)
  Phone: 800-477-8924 or 512-434-1560
  E-mail: support@ti.com
TI E2E Community (videos, forums, blogs)
  http://e2e.ti.com
Embedded Processor Wiki
  http://processors.wiki.ti.com
TI Training
  http://www.ti.com/training
TI eStore
  http://estore.ti.com
TI website
  http://www.ti.com

## Slide 150
www.ti.com/training
Technical Training Organization